ADC

Note: Any function referenced here is in the peripherals/adc.h file, except otherwise stated

Before any further action to the GPIOs, the first thing that must happen is the enabling of the GPIO clock. This is done through the function
void enableADCClocks() (#include “/clock/clock.h”)

Continuous mode
To start the ADC in continuous mode, call the function
void startContinuousConversion(uint8_t sequence[], uint8_t seq_len);
where
- sequence: Is the sequence with which the ADC inputs are sampled
- seq_len: Is the length of the aforementioned sequence

General
To read the data of the last ADC conversion, call the following function, which is blocking and waits until the consversion has ended.
uint16_t readDataConverted();
It returns the value of the last conversion.

GPIOs

Note: Any function referenced here is in the peripherals/gpio.h file, except otherwise stated

Before any further action to the GPIOs, the first thing that must happen is the enabling of the GPIO clock. This is done through the function
void enableGpioClocks() (#include “/clock/clock.h”)
Then, the pin must be configured with the following function
void configPin(uint8_t port, uint8_t pin, uint8_t gpio_mode);
where
- port: Sets the register to be used, e.g. GPIOA for PORTA etc.
- pin: Sets the specific pin to be configured, e.g. GPIO_PIN_1 for pin 1
- mode: Sets the mode, which takes the following values
  - OUTPUT_PUSH_PULL: For output mode with push-pull configuration
  - OUTPUT_OPEN_DRAIN: For output mode with open-drain configuration
  - ALT_FUNC_PUSH_PULL: For output mode with push-pull configuration
  - ALT_FUNC_OPEN_DRAIN: For output mode with open-drain configuration
  - ANALOG: For input mode with analog
  - FLOATING_INPUT: For floating input
  - INPUT_PULL_UP_DOWN: For input with pull-up/pull-down resistors
To set a pin we call
void setPin(uint8_t port, uint8_t pin, uint8_t value);
where
- port: Sets the register to be used, e.g. GPIOA for PORTA etc.
- pin: Sets the specific pin to be configured, e.g. GPIO_PIN_1 for pin 1
- value: Is the value to set (0 for low or 1 for high)

Timers

Note: Any function referenced here is in the peripherals/timer.h file, except otherwise stated

Two usages of timers are implemented. PWM using PA1 pin as output channel, and up/down counting, with the option of using interrupts or not.

To use PWM with output channel PA1, we call
void setPWM(uint8_t frequency);
where:
frequency: user selected frequency value

To use timers for counting purposes, we call
void setTimer(uint32_t timer, uint32_t frequency, uint32_t prescaler,
uint32_t direction, uint32_t intr-en );
where:
- timer: timer selection (options: TIM2,TIM3,TIM4,TIM5)
- frequency: user selected frequency value
- prescaler: prescaler value
- direction: up/down counting direction (options: UP, DOWN)
- intr_en: interrupt selection option (enable:1, disable:0)

Implementation notes:
In our PWM implementation we do not offer any Duty Cycle (DC) customization, or prescaler customization.
DC default value is 50% , and there is no prescaling by default.

For accurate frequency selection, we implemented
uint32_t getTimerClockFreq()
This function returns clock’s frequency.
SetPWM(.) uses this accurate frequency calculation, while setTimer(.) does not.

Interrupts

Note: Any function referenced here is in the peripherals/interrupt.h file, except otherwise stated

We implemented functions for SysTick usage, enabling/disabling interrupts and some interrupt handlers.

For SysTick usage we created the following functions:
void setSystickReload(uint32_t value)
where:
value: reload value of SysTick timer

and
void enableSystick()
which enable SysTick timer.

For enabling/disabling interrupts we created the following functions:
void setInterrupt(uint32_t position)
void clearInterrupt(uint32_t position)
where:
position: set/clear enable NVIC register location (details In interrupt.h)

Finally, we created the following interrupt handlers , for testing and debugging purposes.
We created HardFault_ISR(), TIM2_ISR(), TIM3_ISR(), TIM4_ISR(), TIM5_ISR()